HCP – Holub’s Communication Protocol
6 wires communication protocol
Simple to understand
No timing required (only delay to stabilize levels)
Both-side acknowledge.
No error check.

---
Prologue
Billions of stupid, poorly designed and insecure devices will be connected to the Internet in the near future…
… Many people knowing little to nothing about
electronics/coding/network/security/anything will
ravingly enter the world of IOT.

---
Project motivation
- Verify that it may actually work.
- Create “crystal radio” of IT world.
- Desire to build up communication protocol from
  scratch.
- Being an author makes me actually HCP expert.

---
Wiring
MISO
-----------------------------
MOSI
-----------------------------
SCK
-----------------------------
ACK
-----------------------------
CHIPSELECT (CS)
-----------------------------

---
Set up of I/O
Master	Slave
INPUT	MISO	OUTPUT
OUTPUT	MOSI	INPUT
OUTPUT	SCK	INPUT
INPUT	ACK	OUTPUT
OUTPUT CS	INPUT

---
Communication phases:
- Initial state
- Data transmission (byte is transferred)
- End of the communication

---
Initial state
- All outputs are LOW.
- Waiting till master seth CHIPSELECT to HI.
- Slave checks CHIPSELECT in all waiting loops during the communication to be able to abort all.

---
Initial state - Start of the communication:
Master sets CHIPSELECT to HI.
    Slave starts checking SCK until these gets HI.
    Slave sets ACK HI.
Master sets SCK HI
    Slave starts checking MOSI until these gets HI.
Master sets MOSI HI.
    Slave sets MISO HI.
HIGH = 1
LOW = 0
MISO = HIGH
MOSI = HIGH
SCK= HIGH
ACK= HIGH
CS=HIGH

---
Data transmission M → S
Transfer of the byte:
Master Slave
1] MOSI - set first bit (high = 1, low = 0)
2] SCK toggled (inverted)
3] BIT received from MOSI
4] ACK toggled that bit has been received
5] Repeat above for remaining bits

---
Data transmission S → M
Master Slave
        1 ] MISO - set first bit (high = 1, low = 0)
        2]ACK is toggled
3] BIT received from MISO
4] SCK toggled
5] Repeat above for remaining bits

---
End of the communication
    Slave sets MISO LOW
Master waits for MISO low
Master sets MOSI LOW!
  Slave waits for MOSI LOW!
Master sets SCK LO
   slave waits for SCK LO
   Slave sets ACK LOW
Master waiting for ACK LOW!

---
Communication rules
- Master always starts the communication by setting CS HI.
- Master always sends first byte.
- Byte sent to slave indicates number of function.
- Master and slave must know communication process of every function – depends on application layer.

---
Common functions
- Device name
- Command list
- Echo

---
Function example
Echo [254]
M sends [254]
M sends another byte.
S sends byte back.